## Slide 1: Arduino/C++ Workshop
ECU Robotics Society – Keegan Barnard, Jessica Dippenaar

## Slide 2: Today’s Session - Monday
9am-10am, Introduction to C++ programming fundamentals
11am - 12pm, Introduction to LED control, “Build LED binary counter”, Program optimization (for loops, while loops and iteration loop)
12-12.30pm - Lunch
1-3pm - Dimmable LED project

## Slide 3: Introduction – Arduino 101
Downloadable IDE: https://www.arduino.cc/en/software
Super Starter Kit – Everything you need to get started
Arduino – A open-source electronics platform
  Incorporates a variety of sensors and components for anyone to create projects

## Slide 4: Arduino Integrated Development Environment (IDE)
File:
  Example Sketches
Tools:
  Port Selection
Void Setup:
  Code runs once
Void Loop:
  Code runs repeatably

## Slide 5: C++ Intro
Variables
  Integer:
    E.g. int redLED = 8;
  Float:
    E.g. float redLED = 3.14;
  Strings:
    E.g. myName = “Keegan”;
Commenting (Used to write reminder text)
  E.g. // Drive forward loop

## Slide 6: Number system

## Slide 7: Task Overview – Binary Counter
LED Binary Counter:
  4x LEDs
  4x 330 Ohm resistors
  Breadboard
  Arduino Uno
Useful tips:
  Lead with the Long Leg of the LED
  Resistor is positioned opposite to the direction you read it

## Slide 8: Task Overview – Dimmable LED
Need:
  LED
  330 Ohm resistor
  Potentiometer (variable resistor)
  Breadboard
  Arduino Uno
Useful tips:
  Lead with the Long Leg of the LED
  Resistor is positioned opposite to the direction you read it
  Potentiometer sends an analog value between 0 – 1023
  LED requires an analog write value between 0 – 255
  Need an equation to relate the two above statements for the input commands
(1023,255)
(0,0)
Potentiometer Value
LED Value