## Slide 1: Arduino/C++ Workshop
ECU Robotics Society – Keegan Barnard, Jessica Dippenaar

## Slide 2: Today’s Session - Tuesday
9am-11am Using Simple Servo, Pushbutton, Joystick, Tilt Switch
11am-12pm, Controlling a DC motor, Tilt switch cut off with DC motor
12pm-12.30pm, Lunch
1pm-3pm, Controlling DC motor speed with Joystick and direction with push buttons

## Slide 3: Servo Motor
Using User input to manually change the position of a servo motor

## Slide 4: Pushbutton
Uses one pushbutton switch to control an LED to turn on/off

## Slide 5: Joystick
Comprises of two potentiometers that act as input variables for the X and Y axes
Comprises of a push switch

## Slide 6: Tilt Switch
Uses tilt switch to control LED to turn on/off when flipped

## Slide 7: Task Overview – DC Motor Control
LED Binary Counter:
  L293D Motor Controller
  DC Motor
  Fan Propeller
  Power Supply Module
  Breadboard
  Arduino Uno
Useful tips:
  Power Supply positive/negative pins must be correctly inserted into breadboard
  Power supply jumper needs to be attached to 5V and VCC, otherwise 5V not supplied
  General rule – power and heat management are important – make sure you use controllers and power supplies suited to the motor used in projects

## Slide 8: Motor Control Setup
EN1 controls the speed of the motor – use analogWrite to EN1, need squigly line pin to PWM function
IN1 and IN7 control direction
OUT1 and OUT2 connect to the motor
Pin 4 is ground of supply
+Vmotor is power from power supply

## Slide 9: Task Overview – Dimmable LED
Need:
  LED
  330 Ohm resistor
  Potentiometer (variable resistor)
  Breadboard
  Arduino Uno
Useful tips:
  Lead with the Long Leg of the LED
  Resistor is positioned opposite to the direction you read it
  Potentiometer sends an analog value between 0 – 1023
  LED requires an analog write value between 0 – 255
  Need an equation to relate the two above statements for the input commands
(1023,255)
(0,0)
Potentiometer Value
LED Value

## Slide 10: Task Overview – DC Motor Control + Tilt Switch
LED Binary Counter:
  L293D Motor Controller
  DC Motor
  Fan Propeller
  Power Supply Module
  Breadboard
  Arduino Uno
  Tilt Switch
Useful tips:
  Power Supply positive/negative pins must be correctly inserted into breadboard
  Power supply jumper needs to be attached to 5V and VCC, otherwise 5V not supplied
  General rule – power and heat management are important – make sure you use controllers and power supplies suited to the motor used in projects

## Slide 11: Task Overview – DC Motor Control + Joystick
LED Binary Counter:
  L293D Motor Controller
  DC Motor
  Fan Propeller
  Power Supply Module
  Breadboard
  Arduino Uno
  Joystick
Useful tips:
  Power Supply positive/negative pins must be correctly inserted into breadboard
  Power supply jumper needs to be attached to 5V and VCC, otherwise 5V not supplied
  General rule – power and heat management are important – make sure you use controllers and power supplies suited to the motor used in projects